#### List of Topics

 Internal registers	1
 Memory Map	2
 Signals EPP-1.9	3
 EPP ports for programmers	4
 Modes	5
 Cycles	6
 EXCHANGE N64 <> PC	7
 EPP Time Diagram	8
 Block diagram	9

Internal registers

#		mode	Bits	name	Descriptions
0	RG0	R w	D[7..0]	a[7..0]	Support count address
1	RG1	R w	D[7..0]	a[15..8]	Only 0 bit support count address
2	RG2	R w	D[7..0]	a[23..16]
3	RG3	w	D[2..0]	a[26..24]
3	RG3	R	D3	Don’t use
			D4	Pc	1 = pc can work with DRAM
			D5	Wcf	wcf 1 = was write cart b4000000-b7FFFFFF
			D6	Wdf	1 = was write DRAM
			D7	Rst	1 = power on n64
4	RG4	R w	D[7..0]	Data	Read and write DRAM
	RG5	w	D0	Pc	1 - enable PC mode, DRAM connect to PC
			D1	Cart_on	0 - cart ROM off from n64 / 1 - cart ROM on
			D2	Write_en	0 – DRAM read only / 1 – DRAM write enable
			D[4..3]	Don’t use
			D5	Wcfset	0 – clear wcf, 1 – set wcf
			D6	Wdfset	0 – clear wdf, 1 – set wdf
			D7	Don’t use

Memory Map

Mode	pc	Cart_on	Wcf	B0000000-B3FFFFFF	b4000000-b7FFFFFF
PC	1	0	0	Nothing	Nothing
PC	1	0	1	Cart	Cart
PC	1	1	0	Nothing	Cart
PC	1	1	1	Cart	Cart
N64	0	0	0	DRAM	DRAM
N64	0	0	1	Cart	Cart
N64	0	1	0	DRAM	Cart
N64	0	1	1	Cart	Cart

N.B. Wcf setting to 1 if you wrote to B4XXXXXX area and CART_ON = 1

Signals EPP-1.9

PV-backup use standard EPP-1.9 protocol and EPP_init is only reset of device.

EPP_write	0 – write cycle 1 – read cycle
EPP_addr_stb	0 – write addres
EPP_data_stb	0 – write data
EPP_init	0 – rest
EPP_busy	0 – ready 1-wait
EPP_data[7..0]	Datas of EPP

EPP ports for programmers

Base:=$378	{base addres of EPP}
const rga = 3 ; rgd = 4; rgc = 2; rgs = 1;
rg_addr:=base + rga	{address register }
rg_data:=base + rgd	{data register}
rg_cntr:=base + rgc	{control register}
rg_stat:=base + rgs	{status register}
# In_reg (number of register) data
Rg_addr:=number of register
Result:=rg_data
# Out_reg (number of register, data)
Rg_addr:=number of register
Rg_data:=data
# Set_reg (number of register)
Rg_addr:=number of register
# In_sec ()data
Result:=rg_data
# Out_sec (data)
Rg_data:=data
Out_cntr (data)
Rg_cntr:=data
Out_stat (data)
Rg_stat:=data

Modes

PV-backup can work in 3 difference modes.
1. Game playing from cartridge
2. Game playing from DRAM
3. Game playing from DRAM but cartridge on
4. Debug mode, in this mode n64 can read and write DRAM, read cartridge and exchange information with PC.

Cycles
# Const
Mwrite_on = 4
Mcart_on = 2
Mpc = 1
Msetwcf = $20

# Reset
Rg_cntr:=0
…
delay timeout
…
rg_cntr:=4

## Pc_mode {DEBUG MODE write on, cart on}
Rg_stat:=1
Out_reg(rg5, mwrite_on + mcart_on +1 )
# N64mode
Rg_stat:=1
Out_reg(rg5, mwrite_on + mcart_on)

## Pc_mode {DRAM PLAY MODE}
Rg_stat:=1
Out_reg(rg5, 1 )
# N64mode
Rg_stat:=1
Out_reg(rg5, 0)
## Pc_mode {CART PLAY MODE cart on, wcf =1 }
Rg_stat:=1
Out_reg(rg5, msetwcf + mcart_on +1 )
# N64mode
Rg_stat:=1
Out_reg(rg5, msetwcf + mcart_on)
## Pc_mode {DRAM AND CART PLAY MODE cart on}
Rg_stat:=1
Out_reg(rg5, mcart_on +1 )
# N64mode
Rg_stat:=1
Out_reg(rg5, mcart_on)
# Set_pointer
Out_reg(0,addres[7..0])
Out_reg(1,addres[15..8])
Out_reg(2,addres[23..16])
Out_reg(3,addres[26..24])
# Read_pointer
Addres:=in_reg(0) + in_reg(1) * $100 + in_reg(2) * $10000 + in_reg(3) * $1000000
# Write_datas
Set_pointer
Set_reg(rg4)
Begin of loop
Out_sec(data)
End_loop
# Read_datas
Set_pointer
Set_reg(rg4)
Begin of loop
Data:=in_sec
End_loop
# Read_status
Status:=in_reg(rg3)

EXCHANGE N64 <> PC

PC do	N64 do
Write data to DRAM
Set n64 debug mode
Delay	N64 found DRAM and work
…….	….. / …..
While wcf = 0 do {wait for wcf}
	IN TO BREAK POINT
	Read Write data to DRAM
	Write to b4XXXXXX
Set pc debug mode	While (b0XXXXXX is ROM) do {see N.B.}
Read write DRAM
Set n64 debug mode
Goto line 3	DRAM found
	Read DRAM
	EXIT TO BREAK POINT

N.B. Checking of presents DRAM in the b0XXXXXX area can be:

You can select for you word in cartridge who<> 0 and <>FFFF
For example word b4FFFFFF = 55AA
You write inverse data to B3FFFFFF
($B3FFFFFF):=$AA55

And now, you can alltimes check DRAM for busy (ROM)

IF ($B3FFFFFF)<>$AA55 THEN DRAM is busy

EPP Time Diagram

EPP_SS IS

S0	S1,SA,S0	S1,SD,S0	S1,SD,S0	S1,SA,S0	S1,SR,SR1,S0	S1,SR,SR1,S0
	Wr addr	Wr data	Wr data	Wr addr	Wr DRAM	Rd DRAM

PVBackup Block Diagram